## Slide 1
<Voltage setting>
<P-gamma>
*Voltage 측정 Point : Source PCB
 | Voltage(V)
VDD | 17.6
HVDD | 8.5
VCC18 | 1.8
Vterm | 1.2
VGH | 30
VGL | -8
 | Gamma Ref. | Value(V)
Positive Voltage | Gamma1 | 16.8
 | Gamma2 | 15.5
 | Gamma3 | 14.2
 | Gamma4 | 13.4
 | Gamma5 | 12.4
 | Gamma6 | 11.5
 | Gamma7 | 11.3
 | Gamma8 | 9.3
 | Gamma9 | 7.7
Negative Voltage | Gamma10 | 8.1
 | Gamma11 | 7.4
 | Gamma12 | 5.7
 | Gamma13 | 5.1
 | Gamma14 | 4.3
 | Gamma15 | 3.2
 | Gamma16 | 2.4
 | Gamma17 | 1.3
 | Gamma18 | 0.4
VCOM |  | 7.85

## Slide 2
<CEDS CTRE>
- | Bit No | Packet Name | LCM settling Value | Remarks
CTRS | 0,1 | CK | 11 | 
 | 2 | CTRS[0] | 0 | Indicates the packet is the control packet LLLLLL
 | 3 | CTRS[1] | 0 | 
 | 4 | CTRS[2] | 0 | 
 | 5 | CTRS[3] | 0 | 
 | 6 | CTRS[4] | 0 | 
 | 7 | CTRS[5] | 0 | 
 | 8 | POL | - | Toggle every frame
 | 9 | GSP | - | Gate Start Pulse
 | 10 | CS1 | 0 | POL Changing Detection C/S
 | 11 | LTD1 | 0 | Mode1
 | 12 | LTD0 | 0 | 
 | 13 | H4INV | 0 | 
 | 14 | POL2 | - | Toggle every frame
 | 15 | SHL | 1 | Right to Left Scanning @ Bottom
 | 16 | H2POL | 0 | 
 | 17 | EQ1 | 0 | Equalizer mode control pins EQ=LL (OFF)
 | 18 | EQ2 | 0 | 
 | 19 | CS0 | 0 | POL Changing Detection C/S
 | 20 | SLEW1 | 1 | Normal Power Mode(75%)
 | 21 | SLEW0 | 0 | 
 | 22 | TESTA[0] | 0 | 
 | 23 | TESTA[1] | 0 | 
 | 24 | TESTA[2] | 0 | 
 | 25 | TESTA[3] | 0 | 
 | 26~27 | DMY | 00 | 

## Slide 3
- | Bit No | Packet Name | LCM settling Value | Remarks
CTR1 | 0,1 | CK | 11 | 
 | 2 | SOE_S[0] | 0 | SOE Start packet data (316)  SOE Start time = First data + 319PCLK SOE Pulse Width = 720ns@1.38Gbps
 | 3 | SOE_S[1] | 0 | 
 | 4 | SOE_S[2] | 1 | 
 | 5 | SOE_S[3] | 1 | 
 | 6 | SOE_S[4] | 1 | 
 | 7 | SOE_S[5] | 1 | 
 | 8 | SOE_S[6] | 0 | 
 | 9 | SOE_S[7] | 0 | 
 | 10 | SOE_S[8] | 1 | 
 | 11 | SOE_S[9] | 0 | 
 | 12 | SOE_E[0] | 1 | SOE End packet data (31)  SOE End time = Last data + 35PCLK
 | 13 | SOE_E[1] | 1 | 
 | 14 | SOE_E[2] | 1 | 
 | 15 | SOE_E[3] | 1 | 
 | 16 | SOE_E[4] | 1 | 
 | 17 | SOE_E[5] | 0 | 
 | 18 | SOE_E[6] | 0 | 
 | 19 | SOE_E[7] | 0 | 
 | 20 | TESTB[0] | 0 | 
 | 21 | TESTB[1] | 0 | 
 | 22 | TESTB[2] | 0 | 
 | 23 | TESTB[3] | 0 | 
 | 24 | TESTB[4] | 0 | 
 | 25 | TESTB[5] | 0 | 
 | 26~27 | DMY | 00 | 
<CEDS CTRE>